## Slide 1
TRIDENT
MARINE POLLUTION INTELLIGENCE
Detect > Localise > Attribute > Forecast > Dispatch > Verify
PS-3Y-14 | SDG 14 Life Below Water
Alen K Reji · Chris Jossy Baptist

## Slide 2
THE GAP
Detection is not the problem. Response is.
Everyone builds: upload -> detect -> label -> report.
That tells you the ocean is dirty. You already knew.
A cleanup boat takes four hours to reach the site.
By then the debris has moved kilometres. The coordinates are already wrong.
Nobody asks where it came from.
Cleanup without attribution means it returns next week.
So we built the loop, not the detector.

## Slide 3
ARCHITECTURE
A closed response loop
DETECT Three modalities, because pollution has no single signature
Countable debris (instance segmentation) · amorphous films, which have no edges to box (spectral indices) · and confusers, detected purely so they can be rejected.
LOCALISE Camera pose -> ray/water-plane intersection
A coordinate per object, not per photo. Plus ground sample distance, object size in cm, and real imaged water area.
ATTRIBUTE The same integrator, run backwards
Hindcasts where the debris entered the water. Cleanup becomes accountability.
FORECAST Lagrangian drift on live ocean currents
Where it will be when the boat actually arrives.
DISPATCH Route to predicted positions, human approves every pickup

## Slide 4
TWO SENSORS
Oil detected twice, by different physics
OPTICAL - photographs and drone frames, visible light
Oil is iridescent at low saturation, and it damps capillary waves, so a slick reads as a SMOOTH anomaly inside an otherwise wave-textured sea. Needs no training run at all. Also counts individual debris and scores algal bloom.
SAR - Sentinel-1 and PALSAR radar backscatter
Radar sees no colour. It sees that oil has flattened the sea surface, so the return drops. A trained DeepLabv3+ segmenter. Works at NIGHT, THROUGH CLOUD, and over whole coastlines.
They are kept deliberately separate, never merged.
Feeding a photograph to a model trained on radar backscatter returns a confident mask of nothing. Training also scores L-band and C-band separately: a model strong on one and weak on the other has learned a sensor, not oil.

## Slide 5
DETECTION
We report what we ruled out
On open water, natural features are mistaken for pollution more often than pollution is missed.
Sea foam, sun glint, vessel wakes, Sargassum, shallow seabed. This is why the MARIDA benchmark exists.
So confusers are scored against pollution on equal terms and reported as rejected.
With the discriminating reason, on screen. A severity score is only credible next to what it declined to count.
Oil has no edges. An object detector cannot find it.
Oil damps capillary waves, so a slick is a LOW-texture anomaly, and its film is iridescent at low saturation. Physics, not a bounding box.

## Slide 6
SEVERITY
A number you can argue with
Nobody else computes severity. They threshold a count.
MPSI is five weighted, individually inspectable components: density, hazard load, coverage, persistence, ecological sensitivity.
Every weight lives in one taxonomy file.
Persistence, mass, windage, entanglement and ingestion risk, toxicity, whether a drone may collect it unattended, scrap value. Retuning the system is a data edit.
A ghost net outscores twenty cardboard boxes, and the system can show you why.
Reported with a confidence band. A wide band means the imagery is the problem, not the water.

## Slide 7
DRIFT
The part nobody else has
Live ocean current and wind, free, no API key.
Verified against the Arabian Sea off Kochi: 0.36 m/s southward.
Windage comes from the taxonomy, so buoyancy changes the forecast.
A styrofoam block rides high and takes 4.5% of the wind; a waterlogged net takes 0.5%. Released from the same pixel, they separate measurably in six hours.
Run the same integrator with a negative timestep and it becomes source attribution.
Forward = interception. Backward = who dumped it. One engine, one minus sign.
Measured: debris drifts 9.7 km in six hours. Routing to the photo's coordinates sends the boat to empty water.

## Slide 8
SCALE
Why not just point a satellite at it?
Because a plastic bottle is forty times smaller than a Sentinel-2 pixel.
Sentinel-2 is 10 m per pixel. A bottle is 0.2 m. From orbit you can see oil slicks, algal blooms and large debris rafts - hectares wide. You cannot see litter.
And the revisit time is five days, while debris drifts 9.7 km in six hours.
By the next satellite pass it is 200 km away. A satellite fix alone is a stale coordinate.
So the real system is three tiers - and this is the roadmap.
SATELLITE screens wide area for slicks and rafts -> DRONE confirms and gives object-level coordinates -> BOAT collects. Our SAR mode is tier one; our optical mode is tier two; the mission planner is tier three.
Automated dispatch to the responsible authority is a webhook, not a research problem.
Severity crosses a threshold, the report and coordinates go out. Next on the list.

## Slide 9
DISPATCH
Autonomy with a human in the loop
Waypoints target where debris WILL be at arrival, not where it was photographed.
Measured offset in our demo: 458 m. Capacity- and battery-constrained routing, with the current's drag on each leg.
Hard interlocks that force a human.
Wildlife in frame aborts collection. Ghost nets, drums and glass never auto-collect - the taxonomy says so, not a hardcoded list. Every decision and override is logged.
The executor talks only to a VehicleAdapter interface.
Swap one class and this flies real hardware over MAVLink. The simulator and the real vehicle are interchangeable - we did not fake a drone, we abstracted one.

## Slide 10
BUILD
What is actually running
FastAPI + PyTorch backend, React + MapLibre mission-control UI, live WebSocket telemetry.
55 tests passing. Satellite basemap. Two sensing modes: optical photographs, and a DeepLabv3+ oil segmenter over Sentinel-1 / PALSAR radar.
Radar and optical stay separate on purpose.
Optical reads an iridescent film in visible light. Radar reads oil flattening the sea surface. Feeding a photograph to a backscatter model returns a confident mask of nothing.
Every model assertion carries whether it is trustworthy.
Checkpoint provenance, positional uncertainty radius, severity confidence band - all the way to the screen.

## Slide 11
LIMITS
What we would fix first
The object detector is COCO-pretrained, not fine-tuned.
It finds bottles, cups and glassware; it misses small litter in wide aerial frames. Fine-tuning on TACO is the next step and the class mapping already exists for it.
The physics thresholds were fitted to synthetic scenes, not a labelled set.
The oil checkpoint is not yet trained to convergence - and the system says so on screen rather than hiding it.
We would rather show you the gap than be caught in it.

## Slide 12
Everyone else tells you the ocean is dirty.
We tell you exactly where each piece is, where it came from,
where it will be in six hours, and we dispatch a boat to intercept it
- with a human approving every pickup.
TRIDENT · github.com/ALEN4343/trident